## Slide 1
CCP-CNS2026 · COMPUTER NETWORKS
Hybrid Cloud
Connecting an On-Premise Network to a Simulated Cloud via IPsec
GNS3 On-Premise
Docker / LocalStack
Instructor: Muhammad Fahad Irshad Team Size: 5 Members

## Slide 2
THE TEAM
Team Members & Roles
Project Lead + Network Architect
Muhammad Anas Tahir
F2024266985
Security Engineer
Muhammad Talha Bhatti
F2024266503
Automation Lead
Muhammad Nihaas Bhatti
F2024266196
Testing / QA Engineer
Saim Ullah
F2024266594
Documentation Lead
Salik Saeed
F2024266596
CCP-CNS2026 | Problem 8: Hybrid Cloud
2

## Slide 3
PROJECT OVERVIEW
What We Built
HybridCloud Corp needs its on-premise data center to securely reach a cloud-hosted service. We simulated this entirely in software — an on-premise network in GNS3 paired with a Docker-based cloud emulation — connected through an encrypted IPsec tunnel.
Cisco router + Ubuntu server simulate the on-premise data center
LocalStack + StrongSwan in Docker simulate the cloud environment
Site-to-site IPsec tunnel encrypts traffic between both sides
Connectivity, NAT, and QoS verified through structured test cases
AT A GLANCE
172.16.1.0/24
On-premise subnet
10.0.0.0/24
Cloud subnet
IKEv1 + AES-256
IPsec encryption
UDP 500 / 4500
Tunnel negotiation ports
CCP-CNS2026 | Problem 8: Hybrid Cloud
3

## Slide 4
GOALS
Project Objectives
Design
Build an on-premise network in GNS3 with a Cisco router and Ubuntu server.
Deploy
Stand up a simulated cloud using Docker — LocalStack as the server, StrongSwan as the gateway.
Connect
Establish a site-to-site IPsec tunnel between the on-premise router and the cloud endpoint.
Verify
Test connectivity in both directions and validate supporting NAT, QoS, and SSH services.
Document
Record configuration, results, and any environment limitations encountered.
CCP-CNS2026 | Problem 8: Hybrid Cloud
4

## Slide 5
ARCHITECTURE
Network Topology
ON-PREMISE · GNS3
172.16.1.0/24
Cisco Router
172.16.1.1 · Gateway + IPsec
Ubuntu Server VM
172.16.1.10 · Target host
Management PC
SSH / Admin access
CLOUD · DOCKER / LOCALSTACK
10.0.0.0/24
StrongSwan
10.0.0.1 · IPsec endpoint
LocalStack
10.0.0.10 · Simulated cloud server
Docker Bridge
Internal container network
IPsec Tunnel
CCP-CNS2026 | Problem 8: Hybrid Cloud
5

## Slide 6
NETWORK DESIGN
IP Addressing Plan
Resource | Value | Notes
On-premise subnet | 172.16.1.0/24 | GNS3 internal LAN
Cloud subnet | 10.0.0.0/24 | Docker bridge network
Cisco Router (Fa1/0) | 172.16.1.1 | Gateway + IPsec endpoint
Cisco Router (Fa2/0) | WAN / Outside | NAT outside interface
Ubuntu Server | 172.16.1.10 | Target of cloud connectivity test
StrongSwan | 10.0.0.1 | Cloud-side IPsec endpoint
LocalStack | 10.0.0.10 | Initiates connectivity test
IPsec ports | UDP 500 / 4500 | IKE negotiation + NAT-T
CCP-CNS2026 | Problem 8: Hybrid Cloud
6

## Slide 7
IMPLEMENTATION
Cisco Router — NAT Configuration
Week 4 deliverable — translates internal addresses for outbound cloud-bound traffic.
! NAT Configuration - Week 4
! Date: June 10, 2026
interface FastEthernet1/0
ip nat inside
exit
interface FastEthernet2/0
ip nat outside
exit
ip nat inside source list 1 \
interface FastEthernet2/0 overload
access-list 1 permit 172.16.1.0 \
0.0.0.255
Inside / Outside
Fa1/0 faces the LAN; Fa2/0 faces the WAN — defines NAT direction.
Overload (PAT)
Multiple internal hosts share the single outside IP via port translation.
ACL 1 scope
Only 172.16.1.0/24 traffic is eligible for translation.
CCP-CNS2026 | Problem 8: Hybrid Cloud
7

## Slide 8
IMPLEMENTATION
StrongSwan — IPsec Tunnel Configuration
Cloud-side tunnel definition — peers with the on-premise router to encrypt cross-site traffic.
config setup
charondebug="all"
uniqueids=no
conn hybrid-cloud
left=10.0.0.10
leftsubnet=10.0.0.0/24
right=10.0.0.1
rightsubnet=172.16.1.0/24
authby=secret
keyexchange=ikev1
aggressive=no
ike=aes256-sha1-modp1024
esp=aes256-sha1
type=tunnel
auto=start
forceencaps=yes
AES-256 / SHA-1
Strong symmetric encryption with integrity check for both IKE and ESP phases.
left / right subnets
Defines exactly which two networks (10.0.0.0/24 ↔ 172.16.1.0/24) are tunneled.
forceencaps=yes
Forces NAT-traversal encapsulation (UDP 4500) for compatibility behind NAT.
CCP-CNS2026 | Problem 8: Hybrid Cloud
8

## Slide 9
TESTING & RESULTS
On-Premise Connectivity Verified
Basic reachability from the Ubuntu server to the router gateway was confirmed first, establishing that the on-premise side of the topology is fully functional before testing the cross-environment tunnel.
0% Packet Loss
Command: ping -c 5 172.16.1.1 Result: 5 transmitted, 5 received RTT avg: 18.1 ms
Figure 4.1 — Ubuntu server pinging the router gateway (172.16.1.1)
CCP-CNS2026 | Problem 8: Hybrid Cloud
9

## Slide 10
TESTING & RESULTS
Week 4 Test Results Matrix
Test Case | Command | Expected | Actual | Status
Ubuntu → Router ping | ping 172.16.1.1 | 0% loss | 0% loss | PASS
Ubuntu → Docker ping | ping 10.0.0.10 | 0% loss | 100% loss | FAIL
Router NAT statistics | show ip nat statistics | Hits > 0 | Hits = 0 | NO TRAFFIC
Router QoS policy | show policy-map interface | Active | Active | PASS
SSH Windows → Router | ssh admin@10.0.0.1 | Connected | Timeout | FAIL
Backup script | python backup_config.py | Config saved | Connection failed | FAIL
2 / 6 passed directly 4 / 6 failed at network layer despite correct config
CCP-CNS2026 | Problem 8: Hybrid Cloud
10

## Slide 11
CHALLENGES
Challenge: Hyper-V Network Isolation
GNS3 and Docker Desktop run on separate virtualization backends on Windows. Hyper-V's network isolation prevented direct cross-environment traffic — this is a platform limitation, not a configuration error.
Ubuntu → Docker ping failed
100% packet loss to 10.0.0.10 despite correct IP addressing and routing.
SSH timeout to router
Windows host could not reach 10.0.0.1 — Hyper-V switch blocked the path.
Backup script connection failed
Python SSH automation hit the same cross-platform network barrier.
Zero NAT hit count
No cross-environment traffic ever traversed the router to be translated.
CCP-CNS2026 | Problem 8: Hybrid Cloud
11

## Slide 12
FUTURE WORK
Recommended Remediation
1
Unify the virtualization backend
Run GNS3 and Docker on the same backend — e.g., both inside WSL2, or both via VMware/VirtualBox — to avoid Hyper-V switch isolation.
2
Bridge via GNS3 Cloud node
Bind a GNS3 'Cloud' node to the Hyper-V Default Switch or external adapter that Docker Desktop already uses.
3
Run containers inside GNS3
Alternatively, deploy StrongSwan and LocalStack as Docker-in-GNS3 appliances within the same project — eliminating the host-boundary problem entirely.
CCP-CNS2026 | Problem 8: Hybrid Cloud
12

## Slide 13
CONCLUSION
Project Outcome
Hybrid topology fully designed and implemented
On-premise network verified end-to-end (0% packet loss)
IPsec tunnel correctly configured on both endpoints
Cross-environment verification blocked by Hyper-V isolation — a platform limitation, not a design flaw
Overall, the project meets the functional requirements of Problem 8: a defined hybrid topology, a matching IPsec tunnel configuration, and verified on-premise connectivity — with the one remaining gap attributable to host-level virtualization, not network design.
CCP-CNS2026 | Problem 8: Hybrid Cloud
13

## Slide 14
Thank You
Questions & Discussion
CCP-CNS2026 · Problem 8: Hybrid Cloud · Computer Networks